## Slide 1: SoilDyn: soil interaction in OpenFAST
Loose coupling SoilDyn + SubDyn + ElastoDyn in OpenFAST
  Implementation complete, testing ongoing
SoilDyn
  6x6 Stiffness matrix
  REDWIN DLL: Models 1, 2, 3 - Tested extensively with Model 2
Testing with Phase II model ongoing
Release in next few weeks for general use/testing

## Slide 2: SoilDyn: soil interaction in OpenFAST
Testing / Settings
Testing with modified OC3 monopile
  High frequency interaction between ElastoDyn tower and SoilDyn
  Question: has anyone else found similar issues?
REDWIN Model 2
  no heave or yaw restoring force
  SubDyn does not allow turning off DOF’s, so disable heave and yaw DOF in ElastoDyn (at tower base)
Loose coupling approach requires very small timestep and 1 correction step

## Slide 3: SoilDyn: soil interaction in OpenFAST
Tips
Loose coupling solver interaction is non-trivial
During development, 6x6 stiffness for faster debugging
REDWIN DLL
  Properties and Calibration curve files must be in working directory
  DLL will abort the program on errors without returning